# Text boxes

Figure B

Figure A

Begin by opening all boxes and separate the poles into groups. Check inventory to make sure all pieces are there.

Look at the diagram and lay the poles out on the ground close to where they would go according to the diagram.

Start from one end and build your first arch. Do not insert the B piece that serves as the bottom leg. This will be the last pieces you install. It is easier to build a 7’ tall frame first. See figure A

Attach your net to the frame using the bungee balls. See figure B.

Note: You may also purchase Clips from a hardware store to hang net from the eye hooks.

Add rubber caps to remaining “B” legs and install the legs to one side. See figure C

Add remaining legs to other side.

***Frame must be staked down at the four corners to keep frame from lifting in high winds. If one side is lifted it can cause frame to collapse in on itself. 55 & 70’ Cage should also be staked in the middle.

Figure C

Completed Batting Cage